## Slide 1
LINFO2347 — COMPUTER SYSTEM SECURITY
Network Attacks
& Protections
A practical study of five common network attacks and their countermeasures, deployed on a Mininet-based enterprise topology.
ICMP Sweep
TCP SYN Scan
SSH Brute-force
ARP Poisoning
DNS Reflected DDoS
Project Presentation

## Slide 2
Network Topology
Mininet enterprise network with workstation LAN, internet, and DMZ
ROUTERS
r1 + r2 enforce baseline nftables forwarding rules
SERVERS
HTTP, DNS, NTP, FTP — plus SSH on http / ntp / ftp
ATTACKERS
internet host (external) and ws3 (insider)
LINFO2347 — Computer System Security
2 / 7

## Slide 3
ATTACK 01 / 05 • RECONNAISSANCE
ICMP Ping Sweep
Discovering live hosts in the DMZ from the Internet
▶ ATTACK
Probe every IP in the subnet
HOW IT WORKS
Run from the Internet host (10.2.0.2) against the DMZ 10.12.0.0/24
Send an ICMP echo-request to each host; an echo-reply means the IP is alive
Builds a map of reachable services before launching deeper attacks
$ COMMAND
# from internet host
python3 attack_ICMP.py 10.12.0.0/24
[+] 10.12.0.10 is alive (http)
[+] 10.12.0.20 is alive (dns)
▶ PROTECTION
Rate-limit echo-requests on r2
HOW IT DEFENDS
nftables meter on r2 tracks ICMP echo-requests per source IP
Above 5 packets/second (burst 3), additional probes are dropped
Legitimate pings still work; a sweep is throttled and incomplete
$ RULE
# protect_ICMP.sh — on r2
nft add rule inet icmp_protect rate_limit_icmp \
ip protocol icmp icmp type echo-request \
meter rate_meter \
'{ ip saddr limit rate over 5/second \
burst 3 packets }' drop
LINFO2347 — Computer System Security
3 / 7

## Slide 4
ATTACK 02 / 05 • PORT SCANNING
TCP SYN Port Scan
Identifying open services on a DMZ host without completing a handshake
▶ ATTACK
Half-open scan to fingerprint services
HOW IT WORKS
Send a TCP SYN to each port; a SYN-ACK reply reveals an open port
Reset (RST) is sent immediately so the connection is never established
Stealthier than a full connect() and reveals running services (HTTP, SSH, FTP…)
$ COMMAND
# from internet host
python3 attack_TCP.py 10.12.0.10 1 1024
[+] Port 22/tcp OPEN
[+] Port 80/tcp OPEN
▶ PROTECTION
Rate-limit new SYN packets on r2
HOW IT DEFENDS
nftables meter matches TCP SYN packets in conntrack state new
Above 5/second (burst 3) per source IP, further SYNs are dropped
A full-range scan becomes too slow to be useful, while normal traffic passes
$ RULE
# protect_TCP.sh — on r2
nft add rule inet tcp_protect rate_limit_tcp \
ip protocol tcp tcp flags syn \
ct state new \
meter tcp_scan \
'{ ip saddr limit rate over 5/second \
burst 3 packets }' drop
LINFO2347 — Computer System Security
4 / 7

## Slide 5
ATTACK 03 / 05 • CREDENTIAL ATTACK
SSH Brute-Force
Guessing credentials on a DMZ SSH server using a password wordlist
▶ ATTACK
Password spraying with paramiko
HOW IT WORKS
Loop through a wordlist, attempting one SSH login per password
Demo wordlist is intentionally small — real attackers use millions of entries
Detects success (auth OK), wrong password, or connection drop (firewall)
$ COMMAND
# from internet host
python3 attack_SSH.py 10.12.0.10 \
mininet wordlist.txt
[-] Attempt 9 (admin): wrong password
[+] SUCCESS after 10 attempts: mininet:mininet
▶ PROTECTION
Dynamic blacklist with rate meter
HOW IT DEFENDS
nftables dynamic set ssh_blacklist with a 5-minute timeout
More than 3 new SSH connections/minute → source IP added to the set
All further packets toward port 22 from that IP are dropped on r2
$ RULE
# protect_SSH.sh — on r2
nft add rule inet SSH_protect SSH_blacklist \
tcp dport 22 ct state new \
meter ssh_ratemeter \
'{ ip saddr limit rate over 3/minute }' \
add @ssh_blacklist '{ ip saddr }' drop
LINFO2347 — Computer System Security
5 / 7

## Slide 6
ATTACK 04 / 05 • MAN-IN-THE-MIDDLE
ARP Cache Poisoning
Insider attack from ws3 to intercept traffic between ws2 and r1
▶ ATTACK
Forged ARP replies + transparent forwarding
HOW IT WORKS
ws3 sends gratuitous ARP replies binding the victim IPs to its own MAC
Enables ip_forward and disables ICMP redirects → silent MITM relay
Victims keep working connectivity but every packet flows through ws3
$ COMMAND
# from ws3 (10.1.0.3)
python3 attack_ARP.py 10.1.0.2 10.1.0.1 \
ws3-eth0
[*] MITM configured: ip_forward=1
Sent 10 poisoned ARP replies
▶ PROTECTION
Static, permanent ARP entries on ws2
HOW IT DEFENDS
Pin 10.1.0.1 → r1's real MAC and 10.1.0.3 → ws3's real MAC as PERMANENT
Kernel ignores any incoming ARP reply that would override these entries
MACs are read directly from the Mininet topology and passed to the script
$ RULE
# protect_ARP.sh — on ws2
ip neigh flush dev ws2-eth0
ip neigh replace 10.1.0.1 lladdr $R1_MAC \
dev ws2-eth0 nud permanent
ip neigh replace 10.1.0.3 lladdr $WS3_MAC \
dev ws2-eth0 nud permanent
LINFO2347 — Computer System Security
6 / 7

## Slide 7
ATTACK 05 / 05 • AMPLIFICATION DDoS
DNS Reflected DDoS
Abusing the DMZ DNS resolver as an amplifier to flood a victim
▶ ATTACK
Spoofed queries with amplification
HOW IT WORKS
Send DNS queries with a spoofed source IP (the victim's address)
We assume that ws3 is a compromised machine
Replies return to the victim, not the attacker — bandwidth amplified ×1.6
$ COMMAND
# from ws3
python3 attack_DNS_DDoS.py 10.1.0.2 10.12.0.20 1000
[*] 10000 spoofed queries sent
[*] victim flooded with amplified replies
▶ PROTECTION
Restrict & rate-limit the resolver
HOW IT DEFENDS
Disable recursion / restrict it to the workstation LAN in dnsmasq
nftables meter on r2 caps DNS queries (port 5353) per source IP
BCP 38: drop spoofed packets that don't match the expected source subnet
$ RULE
# protect_DNS.sh — on r2
nft add rule inet dns_protect rate_limit_dns \
udp dport 5353 ct state new \
meter dns_flood \
'{ ip saddr limit rate over 10/second \
burst 5 packets }' drop
# + dnsmasq: no-recursion / local-only
LINFO2347 — Computer System Security
7 / 7